## Slide 1
Locking Phenomena
Reproducing shear locking & volumetric locking
(PowerPoint lay-out made with the help of AI.)

## Slide 2
What is Locking?
Shear Locking
Occurs in bending-dominated problems
Low-order elements (Q1) cannot represent pure bending without spurious shear strains
Element behaves too stiffly — deflection is severely underestimated
Worsens as L/h increases (more slender beam)
Volumetric Locking
Occurs in nearly-incompressible materials (ν → 0.5)
Incompressibility constraint (εᵥₒₗ ≈ 0) cannot be satisfied element-by-element
Pressure field becomes oscillatory (checkerboard pattern)
Worsens as Poisson's ratio approaches 0.5
Common cause: element formulation cannot represent the true deformation field

## Slide 3
Volumetric Locking —Triangle Setup
t(x) = 20000·x₁
1.5 m
1.0
m
4×3 T3 mesh
(12 triangles)
Parameter | Value
Element type | T3 Linear Triangle
Mesh | 4×2 elements (12 triangles)
Domain | 1.5 × 1.0 mm
Young's modulus | 200 000 MPa
Poisson's ν | 0.3 → 0.49999999
BCs | Fixed left + bottom; traction top
Traction | t(x) = 20 000·x₁

## Slide 4
Volumetric Locking - Background

## Slide 5
Pressure
Volumetric Strain

## Slide 6
Volumetric Locking — Max Displacement vs ν
-1
-2
-3
-4
-5
-6
log₁₀(δ)
-1.0
0.3
-1.1
0.4
-1.3
0.45
-1.7
0.49
-2.5
0.499
-3.5
0.4999
-4.5
0.49999
-5.5
0.499999
Raw Results
ν | Max δ (mm)
0.3 | 9.57 × 10⁻²
0.4 | 7.18 × 10⁻²
0.45 | 4.97 × 10⁻²
0.49 | 1.95 × 10⁻²
0.499 | 2.95 × 10⁻³
0.4999 | 3.13 × 10⁻⁴
0.49999 | 3.15 × 10⁻⁵
0.499999 | 3.15 × 10⁻⁶
X-axis: Poisson ratio ν. Y-axis: log₁₀(max displacement).

## Slide 7
Problem Setup: Cantilever Beam
Beam (L × h = L × 1)
P = 1000 N
(tip load)
L (varies: 1, 2, 4, 8, 12, 16, 20 mm)
Parameter | Value
Element type | Q1 Quadrilateral
Mesh | 4 × 1 elements
Height h | 1 mm
Young's modulus E | 200 000 MPa
Poisson's ν | 0.3 / 0.4 / 0.45 / 0.49 / 0.4999
BCs | Fully fixed left end

## Slide 8
Shear Locking — Background
Beam Shear Stress:
In FEM:
=== L = 20.0 | Bottom nodes (y=h/2) ===
x | σ_xx FEM | σ_xx Exact | σ_12 FEM | σ_12 Exact
0.0 | 110874.3 | -120000.0 | 1064.0 | 0.0
5.0 | 91684.5 | -90000.0 | 976.6 | 0.0
10.0 | 59701.6 | -60000.0 | 1000.0 | 0.0
15.0 | 27718.6 | -30000.0 | 993.6 | 0.0
20.0 | 8528.8 | -0.0 | 995.7 | 0.0

## Slide 9
Shear Locking — Tip Deflection vs Beam Length
Chart: 
| L=1 | L=2 | L=4 | L=8 | L=12 | L=16 | L=20
ν=0.30 | 1.3684 | 0.845 | 0.6094 | 0.3514 | 0.2093 | 0.1338 | 0.0914
ν=0.40 | 1.1546 | 0.616 | 0.4375 | 0.2866 | 0.1886 | 0.128 | 0.0907
ν=0.45 | 0.9831 | 0.435 | 0.2832 | 0.2016 | 0.1478 | 0.1086 | 0.0811
ν=0.49 | 0.8024 | 0.2435 | 0.103 | 0.065 | 0.0541 | 0.0467 | 0.0405
ν=0.4999 | 0.7505 | 0.1881 | 0.0475 | 0.0123 | 0.0058 | 0.0035 | 0.0025
Ratio = 1.0
(perfect accuracy)
Key Observations
Ratio drops sharply as L/h increases
At L=20, ν=0.3: only 9% of correct deflection captured
This is shear locking: bending activates spurious shear strains
Effect present even at ν=0.3
Y-axis: FEM tip deflection / Analytical (Euler-Bernoulli). Value = 1 → exact. Value < 1 → locking.

## Slide 10
Locking Severity Map — FEM/Analytical Ratio
L / h | ν=0.30 | ν=0.40 | ν=0.45 | ν=0.49 | ν=0.4999
L = 1 | 1.368 | 1.155 | 0.983 | 0.802 | 0.750
L = 2 | 0.845 | 0.616 | 0.435 | 0.243 | 0.188
L = 4 | 0.609 | 0.438 | 0.283 | 0.103 | 0.048
L = 8 | 0.351 | 0.287 | 0.202 | 0.065 | 0.012
L = 12 | 0.209 | 0.189 | 0.148 | 0.054 | 0.006
L = 16 | 0.134 | 0.128 | 0.109 | 0.047 | 0.004
L = 20 | 0.091 | 0.091 | 0.081 | 0.041 | 0.003
≥ 0.9 Accurate
0.5–0.9 Moderate locking
0.2–0.5 Severe locking
< 0.2 Extreme locking

## Slide 11
Why Does Locking Occur? The Mechanism
Shear Locking Mechanism
Q1 element has linear displacement field in each parametric coordinate
Bending requires quadratic terms
Q1 can only represent linear terms
The missing quadratic terms appear as parasitic shear ε_xy
→ Element cannot bend without being 'pulled' by shear
→ Structure appears artificially stiff
Volumetric Locking Mechanism
Nearly incompressible: εᵥₒₗ = ε_xx + ε_yy ≈ 0 everywhere
Each element must independently satisfy εᵥₒₗ ≈ 0
With n elements: n constraints on limited DOFs
System becomes overconstrained (too many constraints)
Displacement field becomes artificially stiff (locking)
→ Pressure field oscillates wildly (checkerboard)

## Slide 12
Volumetric Locking — Effect of Poisson's Ratio
Chart: 
| ν=0.30 | ν=0.40 | ν=0.45 | ν=0.49 | ν=0.4999
L=2 | 0.845 | 0.616 | 0.435 | 0.2435 | 0.1881
L=4 | 0.6094 | 0.4375 | 0.2832 | 0.103 | 0.0475
L=8 | 0.3514 | 0.2866 | 0.2016 | 0.065 | 0.0123
L=16 | 0.1338 | 0.128 | 0.1086 | 0.0467 | 0.0035
Key Observations
Ratio collapses as ν → 0.5
At ν=0.4999, L=16: only 0.35% of correct deflection
Incompressibility constraint over-stiffens element
Shear & volumetric locking act simultaneously
Y-axis: FEM / Analytical deflection ratio. Both axes show that locking worsens in combination.